## Slide 1
Data Acquisition, Processing & Edge Computing Systems
Systems Engineering Division

## Slide 2
TRAINING OUTCOMES
Ingestion
Master multi-channel signal capture and hardware synchronization.
Edge Logic
Develop real-time processing and local state machine logic.
Telemetry
Architect robust Edge-to-Cloud telemetry data pipelines.

## Slide 3
INDUSTRIAL CONTEXT
In modern factories, Data Acquisition (DAQ) is the "Sensory Nervous System" of the enterprise.
Safety: Real-time fault detection.
Yield: Precision tuning of variables.
Downtime: Predictive analytics to avoid machine failure.

## Slide 4
THE 4-LAYER STACK
Modern IoT architecture logically separates data flow into manageable engineering silos:
Perception: Physical sensor interaction.
Network: Protocol translation & transport.
Processing: Edge filtering & Cloud DB.
Application: Dashboards & HMI logic.

## Slide 5
THE DIGITAL PIPELINE
Sequential Transformation
1.
Transducer: Physics to Electrical.
2.
Conditioner: Filter & Amplification.
3.
ADC: Analog to Digital Bits.
4.
Driver: Register to Memory Array.

## Slide 6
SIGNAL CONDITIONING
Cleaning the Edge
Raw signals are often weak (μV range) and noisy. Hardware pre-processing is mandatory.
InAmp: High CMRR to reject EMI.
Filtering: Eliminating high-freq jitter.
Isolation: Protecting the processor from kilovolt spikes.

## Slide 7
ANALOG NOISE MANAGEMENT
Differential Advantage
By subtracting two inverse lines (A-B), industrial systems cancel noise that hits both wires simultaneously.
Crucial for: Long cable runs (>10m) across noisy motor control centers.

## Slide 8
MULTICHANNEL INGESTION
Hardware Sharing
Multiplexing allows a single expensive high-resolution ADC to process dozens of sensors.
Addressing: Logic lines select the active sensor.
Switching: High-speed MOS switches ensure minimal crosstalk.

## Slide 9
QUANTIZATION ENGINES
SAR vs. Delta-Sigma
SAR: Moderate speed, high efficiency. The workhorse of standard microcontrollers.
Delta-Sigma: Slow but extreme resolution (24-bit). Ideal for scientific weighing and audio.

## Slide 10
SYNCHRONOUS BUS: SPI
The Gold Standard for DAQ
Serial Peripheral Interface (SPI) provides the deterministic, high-speed link needed for raw sensor data.
Full-duplex (simultaneous Rx/Tx).
Speeds up to 100MHz+ possible.
Hardware chip-select for zero address lag.

## Slide 11
FIELDBUS: RS-485
Industrial Reliability
For connectivity spanning up to 1.2km, RS-485 is the industry's resilient choice.
Differential pair: Immune to EMI.
Multi-drop: Connect up to 32 nodes on a simple twisted pair cable.

## Slide 12
Edge Computing
Intelligence at the Hardware Boundary

## Slide 13
THE PLATFORM: RPI 5
Production-Ready Edge
The Raspberry Pi 5 transitions from "maker gadget" to a high-performance Edge Node.
Cortex-A76: Performance cores for AI.
RP1 Southbridge: Deterministic GPIO control.
PCIe: High-speed NVMe storage.

## Slide 14
THE SOFTWARE STACK
Architecting for Stability
Kernel Space: Low-level hardware drivers.
User Space: Python/C++ Application logic.
Real-time patches: (PREEMPT_RT) for sub-millisecond determinism.

## Slide 15
DETERMINISM ANALYSIS
Jumping to Action
Polling: CPU repeatedly checks a pin. High waste, high latency variation.
Interrupts: Hardware triggers the CPU. Sub-microsecond response, perfect for high-speed alarms.

## Slide 16
DIRECT MEMORY ACCESS
Bypassing the CPU
DMA allows hardware to dump data straight to RAM without core processor intervention. Mandatory for high-speed logging.
CPU Load: 0% for data movement.
Efficiency: Direct peripheral-to-memory block transfers.

## Slide 17
IN-MEMORY RING BUFFERS
Handling Data Spikes
Circular arrays decouple the high-priority Producer (ADC) from the slower Consumer (Cloud Upload).
Constant memory footprint.
Zero dynamic allocation (no heap fragmentation).

## Slide 18
LOCAL AI INFERENCE
Intelligent Boundary
Moving machine learning to the Edge reduces cloud bandwidth by 99% and latency to milliseconds.
CNNs: For real-time visual inspection.
FFT: For frequency-domain anomaly detection.

## Slide 19
MODEL QUANTIZATION
Converting 32-bit weights to 8-bit integers increases speed by 3x on Edge hardware with minimal accuracy loss.

## Slide 20
BACKBONE: MQTT
Pub-Sub Paradigm
The standard "language" for Edge-to-Cloud connectivity.
Decoupled: Sensors don't need to know where the cloud is.
QoS: Built-in delivery guarantees.
Payload: Supports Binary or JSON.

## Slide 21
PAYLOAD EFFICIENCY
JSON vs. Protobuf
Industrial cellular links are expensive. Protocol Buffers reduce data usage by up to 10x compared to text-based JSON.

## Slide 22
LAMBDA ARCHITECTURE
The Dual Path
Hot Path: Live data bypassed directly to real-time dashboards (low latency).
Cold Path: Raw logs archived for deep historical auditing and ML training.

## Slide 23
STORAGE: TSDB
Optimized for Chronology
Standard SQL fails under millions of concurrent sensor writes. TSDBs (InfluxDB) use Columnar Compression.
Rapid time-range queries.
Automated data aging rules.

## Slide 24
SECURING THE EDGE
Mutual Identity
IoT nodes are physical targets. Mutual TLS (mTLS) ensures that only verified nodes talk to the cloud, and vice-versa.
RoT: Keys must be stored in hardware secure elements.

## Slide 25
OPERATIONAL INSIGHTS
Grafana HMI
The ultimate view of your Edge network. Combines real-time telemetry with threshold alerts.
Rolling line charts.
Color-coded health gauges.
Global fleet map views.

## Slide 26
Masterclass Summary
Integrating robust physical ingestion with intelligent Edge processing and secure Cloud synergy creates the modern industrial edge.
Q&A SESSION | TRAINING COMPLETE