## Slide 1
Raspberry Pi Architecture & Embedded Linux
Fundamentals for Industrial Systems & Edge Computing

## Slide 2
TRAINING OUTCOMES
Hardware Literacy
Master the silicon architecture of the Broadcom BCM2712 SoC and high-speed I/O busses.
OS Proficiency
Learn to navigate Embedded Linux kernels, filesystem structures, and Shell programming.
System Engineering
Build and deploy industrial-grade data loggers and HMIs using professional workflows.

## Slide 3
WHY SINGLE BOARD COMPUTERS?
The Raspberry Pi 5 has bridged the gap between a hobbyist board and a robust industrial compute node.
Versatility: Runs a full Linux stack while providing direct hardware I/O control.
Ecosystem: Millions of developers and standardized libraries reduce time-to-market.
Reliability: 10+ year availability for industrial-grade Compute Modules.

## Slide 4
INDUSTRIAL FOOTPRINT
From smart factories to hospital monitoring, Embedded Linux is everywhere.
Edge Gateways: Aggregating PLC data and pushing to Cloud (Azure/AWS).
Industrial HMIs: Driving interactive touch-panels on the factory floor.
Predictive Maintenance: Real-time vibration and thermal analysis.

## Slide 5
THE LEGACY SILO PROBLEM
Legacy Systems
Proprietary machines, manual data logging, high maintenance costs, and zero cloud visibility.
The Linux Solution
Open standards, real-time telemetry, automated control loops, and unified remote management.

## Slide 6
Fundamental Concepts
SoC Architecture & Hardware Operating Principles

## Slide 7
THE SOC FUNDAMENTALS
System-on-Chip (SoC)
Unlike traditional PCs with discrete components, an SoC integrates the CPU, GPU, RAM, and I/O controllers into a single silicon substrate.
Why it's used: Massive power efficiency, lower thermal footprint, and high-speed internal bus communication.
The Broadcom BCM2712 is the heart of RPi 5, featuring quad-core ARM Cortex-A76 performance.

## Slide 8
GPIO: THE PHYSICAL LINK
GPIO (General Purpose Input/Output) pins allow the Raspberry Pi to interact with the analog world.
Pins: 40-pin header for digital I/O.
Logic: 3.3V Logic level (Strictly non-5V tolerant).
Multi-function: Can be configured for UART, SPI, or I2C communication.

## Slide 9
RPI VS TRADITIONAL PC
Feature | Standard Desktop (x86) | Single Board Computer (ARM)
Architecture | Complex (CISC) | Reduced (RISC)
Storage | SATA / NVMe SSD | MicroSD / PCIe NVMe
Power | 150W - 600W | 15W - 25W
I/O | USB / PCIe / Thunderbolt | GPIO / I2C / SPI / MIPI

## Slide 10
POWER OPERATING PRINCIPLES
Technical Specs
The Raspberry Pi 5 requires a 5V / 5A USB-C PD supply for peak performance. The dedicated DA9091 PMIC manages internal voltages for the SoC cores, LPDDR4X, and I/O banks.
Limitation: Inadequate power results in "Under-voltage" throttling, causing system instability.
Supports Power Delivery (PD) to negotiate higher currents for external USB peripherals.

## Slide 11
Core Architecture
Silicon, Memory, and the RP1 Southbridge

## Slide 12
BCM2712 DEEP DIVE
The Compute Engine
3x performance increase over Raspberry Pi 4 due to re-architected pipelines.
CPU: Quad-core ARM Cortex-A76 (2.4GHz).
GPU: VideoCore VII (OpenGL ES 3.1).
Bus: Internal AXI bus fabric for low-latency memory access.

## Slide 13
THE RP1 CONTROLLER
Custom Silicon
For the first time, RPi uses in-house silicon for I/O. The RP1 manages Ethernet, USB 3.0, and GPIO, connected to the main SoC via PCIe lanes.
Impact: Massive bandwidth boost for all external peripherals without taxing the main CPU cores.

## Slide 14
LPDDR4X MEMORY SUBSYSTEM
Bandwidth
LPDDR4X-4267 SDRAM providing peak bandwidth of 17 GB/s.
Unified RAM
GPU and CPU share the same memory pool (User-configurable split).
Capacity
Available in 1GB to 8GB variants for diverse compute loads.

## Slide 15
EXPANSION & HIGH-SPEED I/O
PCIe Gen 2.0 x1
The RPi 5 exposes a single PCIe lane, enabling direct connection to NVMe SSDs and high-speed network cards via HATs.
Ethernet: Dedicated RGMII interface for full 1Gbps throughput.

## Slide 16
Embedded Linux Foundations
Kernel Architecture, Shell & Filesystems

## Slide 17
THE LINUX KERNEL LAYERS
The Kernel acts as the "Manager" between User Applications and Physical Hardware.
User Space: Shell, Python, User Apps.
Kernel Space: Process scheduling, Drivers.
Hardware Abstraction: Unified interface for sensors.

## Slide 18
FILESYSTEM HIERARCHY (FHS)
/bin & /sbin: Essential binaries.
/etc: Configuration files.
/dev: Hardware devices as files.
/var: Variable data (logs/caches).
/proc & /sys: Virtual filesystems for kernel info.

## Slide 19
THE LINUX BOOT SEQUENCE

## Slide 20
LINUX DISTRIBUTIONS (DISTROS)
Raspberry Pi OS
Standardized, Debian-based, easy to use for rapid development.
Ubuntu Core
Security-focused, transactional updates for mass IoT deployment.
Yocto / Buildroot
Custom industrial Linux. Extremely small and highly specialized.

## Slide 21
Technical Deep Dive
Device Trees, systemd & Shell Mastery

## Slide 22
DEVICE TREE OVERLAYS
A Device Tree (DT) is a data structure describing hardware to the Kernel. Overlays allow you to add peripherals at runtime without re-compiling the kernel.
Enables the same Kernel to run on hundreds of different board revisions.

## Slide 23
THE SYSTEMD INIT SYSTEM
systemd manages background services (daemons). It ensures your IoT application starts automatically after a power failure.
sudo systemctl status my_app.service
The standard way to monitor, stop, and start industrial application flows.

## Slide 24
BASH SCRIPTING AUTOMATION
Industrial reliability requires automated tasks. Use Bash for hardware monitoring and log rotation.

## Slide 25
Implementation Workflow
Configuration, Programming & Toolchains

## Slide 26
HEADLESS SETUP (SSH)
Most industrial nodes run without a monitor (Headless). We use SSH (Secure Shell) for configuration.
Command: ssh pi@192.168.1.10
Tool: raspi-config for CLI interface setup.
Connectivity: Static IP or MDNS (.local) addressing.
Remote: SCP/SFTP for file transfers.

## Slide 27
DEVELOPMENT TOOLCHAINS
Python / pip
High-level libraries like paho-mqtt and gpiozero.
C / C++ (GCC)
For high-performance drivers and memory-critical tasks.
Node-RED
Visual programming for rapid dashboarding and logic flow.

## Slide 28
USE CASE: OPERATOR HMI
Visual Interface
Using RPi 5 to drive industrial touch-screens. Kiosk mode Chromium allows web-based dashboards to act as local controllers for PLCs.
Real-time OEE Dashboard.
Digital Work Instructions.

## Slide 29
USE CASE: IOT GATEWAY
Data Bridge
Acts as the bridge between legacy serial devices (RS-485/Modbus) and modern Cloud servers. It provides local buffering and encryption.
Impact: Secure, stable connectivity for brown-field factory floors.

## Slide 30
USE CASE: EDGE AI
Local Inference
Running Neural Networks (TensorFlow Lite) directly on RPi 5 to identify defects in manufacturing without cloud latency.
Benefit: 100% Privacy and Zero dependency on internet uptime.

## Slide 31
Mini Project
Industrial Edge Data Logger Implementation

## Slide 32
PROJECT COMPONENTS
Objective: Track vibration and temperature trends to predict motor failure.
Gateway: Raspberry Pi 5.
Sensors: MPU6050 & BME280 (I2C).
Protocol: MQTT (HiveMQ Broker).
Visualization: Grafana Dashboard.

## Slide 33
WORKING PRINCIPLE
1. Polling: Python script reads I2C busses every 1s. 2. Formatting: Data converted to JSON. 3. Pub/Sub: Published to factory/vib topic. 4. Auto-start: Systemd ensures service resilience.

## Slide 34
TECHNICAL INTERVIEW PREP
What is the significance of the /proc filesystem in Linux?
How does an I2C protocol address 127 different devices?
Differentiate between Kernel Space and User Space.
What is a Device Tree Overlay and why is it used for HATs?
Explain the "systemd" unit file structure for an IoT app.

## Slide 35
Summary & Conclusion
Architecture | Linux | Industrial IoT
The connected industrial future is open, modular, and Linux-powered.
Q & A SESSION