## Slide 1
Sensor Interfacing & Real-Time DAQ
Bridging Physical Phenomena and Digital Reality
A Comprehensive Training for Future Systems Engineers

## Slide 2
TRAINING OUTCOMES
Hardware Master
Master transduction and physical signaling standards.
Signal Logic
Design precision conditioning and hardware filtering.
Real-Time DAQ
Implement deterministic sampling and DMA flow.

## Slide 3
THE INDUSTRIAL DAQ CORE
Data Acquisition (DAQ) forms the nervous system of modern automation.
Safety: Real-time monitoring prevents machine failure.
Optimization: Granular data allows for precision tuning.
Predictive: Catching bearing wear before it breaks.

## Slide 4
THE FUNCTIONAL PIPELINE
Digital transformation follows a strict sequential path:
1.
Transducer: Physical to Electrical.
2.
Conditioning: Filtering & Scaling.
3.
ADC: Analog to Digital Bits.
4.
Driver: Register to Software Array.

## Slide 5
PHYSICS OF TRANSDUCTION
Energy Conversion
Sensors exploit physical properties like Resistance, Capacitance, and Piezoelectricity to convert mechanical/thermal energy into micro-currents or voltages.

## Slide 6
THERMAL STATE ACQUISITION
Thermocouples vs RTDs
Thermocouples: Robust, Wide Range, based on Seebeck Effect.
RTDs: Platinum resistance shifts (PT100). High accuracy, limited range.

## Slide 7
PRESSURE & FORCE
Differential Logic
Industrial pressure cells measure the strain on a diaphragm. Integrated electronics scale the micro-mV signals into standard loops.

## Slide 8
STRAIN GAUGE INTERFACING
Micro-Deflection Detection
Resistance changes linearly with mechanical stress. Because the shift is tiny, we use a Wheatstone Bridge to extract a measurable differential voltage.

## Slide 9
VIBRATION & MEMS
Micro-Machine Systems
MEMS sensors integrate the spring-mass system directly on silicon. Essential for high-frequency vibration harmonics tracking (>10kHz).

## Slide 10
OPTICAL & PROXIMITY
Non-Contact Telemetry
LiDAR and Laser sensors calculate distance using Time-of-Flight (ToF). Requires precise nanosecond timing and pulse shaping.

## Slide 11
ACTIVE VS PASSIVE SIGNALS
Active: Generates own EMF (Thermocouple). No external power for signal.
Passive: Requires excitation (RTD). Resistance shift must be "driven" by current to see volts.

## Slide 12
OP-AMP ARCHITECTURE
High-Precision Scaling
Raw signals are too weak for ADCs. Op-Amps provide:
Buffering: No signal loss to ADC input impedance.
Gain: Multiplying microvolts to standard 0-5V levels.

## Slide 13
DIFFERENTIAL SIGNALING
Noise Rejection
Industrial noise hits both lines equally. By taking the difference (A-B), we cancel out the common-mode interference completely.

## Slide 14
BRIDGE CALIBRATION
Null Balancing
Real hardware has offsets. Calibration involves adjusting bridge legs to ensure 0V output at 0 physical stress, maximizing dynamic range.

## Slide 15
HARDWARE FILTERING
Cleaning the Edge
Hardware Low-Pass Filters (LPF) are mandatory before ADC to remove high-freq jitter and prevent signal Aliasing.

## Slide 16
GALVANIC ISOLATION
Optical Protection
Isolating the high-voltage factory floor from sensitive logic. Signals pass as light pulses across an air gap. No electrical connection = Total safety.

## Slide 17
NYQUIST SAMPLING THEORY
F_s > 2 * F_m
To accurately capture a waveform, you must sample at at least twice the highest frequency. In industry, we oversample 10x for safety.

## Slide 18
THE ALIASING HAZARD
Spectral Plotting
Sampling too slowly creates "ghost" frequencies that do not exist in the real signal. This data corruption is irreversible in software.

## Slide 19
QUANTIZATION ERROR
Rounding Realities
The gap between the real voltage and the digital bit. More bits = smaller steps. 12-bit is industrial standard (4096 levels).

## Slide 20
SAR ADC ARCHITECTURE
Binary Search Logic
Successive Approximation Register (SAR) ADCs balance speed and power. They find the correct bit value by testing half-steps until convergence.

## Slide 21
DELTA-SIGMA MODULATION
Noise Shaping
Uses extreme oversampling (1-bit) and digital decimation filtering to achieve 24-bit resolution. Perfect for high-fidelity audio and weighing scales.

## Slide 22
HIGH SPEED BUS: SPI
Full-Duplex Master-Slave
Fastest board-level bus (>50MHz). 4 wires: SCK, MOSI, MISO, CS. Essential for high-resolution ADC streaming.

## Slide 23
INTERFACE: I2C
Multi-Drop Networking
Uses only 2 wires (SDA/SCL) and software addressing. Supports up to 127 sensors on one bus segment. Ideal for low-speed peripherals.

## Slide 24
BUS SELECTION MATRIX
Metric | I2C | SPI | RS-485
Wires | 2 | 4+ | 2 (Diff)
Distance | <5m | <3m | >1000m
Speed | 400kbps | 50Mbps+ | 10Mbps
Nodes | 127 | Line-limited | 32-256

## Slide 25
DIRECT MEMORY ACCESS
Freeing the CPU
DMA allows the ADC to dump data directly into RAM arrays without CPU intervention. Critical for multi-MHz sampling rates.

## Slide 26
INTERRUPT CONTROL
Deterministic Jumps
Instead of "polling" a sensor, we jump to an Interrupt Service Routine (ISR) immediately when a signal threshold is hit.

## Slide 27
CIRCULAR RING BUFFERS
Producer-Consumer Logic
Prevents data loss during network spikes. ADC writes to the head, App reads from the tail. Data wraps around automatically.

## Slide 28
TIMING JITTER
Real-Time Stability
Sampling intervals must be perfect. Software timers have jitter. Hardware Timer-Triggers for ADC ensure absolute temporal precision.

## Slide 29
INDUSTRIAL GROUNDING
The Star-Ground Rule
Ensure all analog sensor grounds meet at a single physical point to eliminate differential potentials between machines.

## Slide 30
STATE ESTIMATION
Software Filtering
Hardware can't clean everything. Kalman Filters use physical models to "guess" the true value among noisy readings.

## Slide 31
PRACTICAL CASE STUDY
Motor Vibration Link
Build an RPi logger that samples high-freq vibration, filters via EMA (Exponential Moving Avg), and pushes to cloud via MQTT.

## Slide 32
Mastering the Edge
Sensors are the eyes of automation. Quality DAQ is the key to autonomy.
Q&A SESSION | PROFESSIONAL TRAINING SERIES