## Slide 1
Cybersecurity & Secure IoT System Design
Hardware Security, Cryptography, & Device Hardening

## Slide 2
COURSE MODULES
Hardware Roots
Securing the physical boundary through Secure Boot, PUFs, and Cryptographic Co-processors.
Transport Security
Implementing mutual TLS authentication, payload encryption, and lightweight cipher suites.
Lifecycle Security
Managing cryptographically signed over-the-air firmware modifications and key revocation frameworks.

## Slide 3
THE UNIQUE VULNERABILITIES OF IOT
Unlike standard enterprise endpoints, IoT devices operate at a high risk of compromise due to their physical exposure.
Physical Threat Vector: Adversaries can buy field nodes, probe memory traces, or force fault injections.
Resource Constraints: Low-power microcontrollers lack the memory space needed for massive asymmetric crypto libraries.

## Slide 4
HARDWARE ROOT OF TRUST (ROT)
The Anchor of Trust
Security must start in hardware. Software protections mean nothing if the underlying silicon layer is compromised.
Secure Element (SE): An isolated hardware vault designed to shield private keys from the application code.
Hardware Cryptographic Accelerators: Offload resource-intensive AES-256 and ECC math operations to dedicated silicon logic gates.

## Slide 5
PHYSICALLY UNCLONABLE FUNCTIONS (PUF)
Silicon Fingerprinting
Storing static cryptographic keys in digital flash memory creates a vulnerability to physical readout attacks.
The Mechanism: A PUF leverages atomic micro-variations introduced during wafer fabrication to form a unique hardware signature.
The Advantage: Keys are generated on-demand from silicon characteristics and disappear instantly when power is removed, leaving nothing for attackers to dump.

## Slide 6
THE IMMUTABLE SECURE BOOT CHAIN
Establishing Chain of Custody
Secure Boot stops unauthorized or altered code from executing during the initialization process.
Stage 0 (Mask ROM): Code burned directly into silicon that cannot be altered. It holds the root public key.
Verification Steps: Every boot stage calculates a SHA-256 hash of the next stage's payload, verifying it against a digital signature before executing.

## Slide 7
LIGHTWEIGHT CRYPTOGRAPHY CIPHERS
Cipher Target | Structural Type | Memory Resource Footprint | Primary IoT Application Scenario
AES-128 / GCM | Symmetric Block | Moderate ($4\text{--}8\text{ KB}$) | Standard gateway nodes with hardware acceleration blocks
ChaCha20 / Poly1305 | Symmetric Stream | Low ($2\text{--}4\text{ KB}$) | Ultra-low-power devices lacking dedicated hardware ciphers
ASCON (NIST Standard) | Authenticated Encryption | Extremely Low ($<1.5\text{ KB}$) | Resource-constrained smart sensor tags running on minimal energy
ECC (ECDSA P-256) | Asymmetric Public-Key | High ($12\text{--}24\text{ KB}$) | Securing handshake protocols and verifying OTA firmware signatures

## Slide 8
MUTUAL TLS HANDSHAKE MECHANICS
Dual-Sided Verification
Standard web browsing requires only the user to verify the server's identity. Secure IoT systems mandate **Mutual Authentication (mTLS)**.
The cloud endpoint verifies the unique X.509 certificate stored in the node's secure hardware.
The node verifies the cloud server's root certificate bundle, neutralizing potential Man-in-the-Middle (MitM) interceptions.

## Slide 9
HARDENING EDGE DEVICE INTERFACES
Closing Physical Backdoors
Unused diagnostic entry points on physical circuit boards are frequently targeted by malicious reverse-engineers.
JTAG/SWD Disabling: Production firmware must blow internal silicon fuses to permanently deactivate debugging access before field deployment.
Console Gating: Serial UART console lines must be password-protected or entirely muted in production builds.

## Slide 10
SECURE OVER-THE-AIR (OTA) UPDATES
Defending Firmware Distribution
Flashing new code remotely introduces a critical risk of complete system takeover if unauthorized binaries are accepted.
Asymmetric Signing: Firmware blobs must be compiled and signed offline inside a secure build facility using a private RSA/ECDSA key.
Device Validation: The target device uses its embedded public key to verify the binary signature before writing it to a flash partition.

## Slide 11
DUAL-PARTITION ANTI-BRICK ROLLBACKS
Resilient Recovery Design
A failed firmware write can easily brick a remote node, requiring expensive manual field recovery.
A/B Memory Partitioning: Devices maintain two distinct runtime banks. The active system executes from Bank A, while the update writes to Bank B.
Automated Fallback: If the updated image fails to boot or clear watchdogs, the bootloader safely reverts control back to the known stable partition.

## Slide 12
THE RISK OF REPLAY ATTACKS
Preventing Command Interception
Even if an attacker cannot decrypt a payload, they can capture a valid ciphertext command (such as "Unlock Gate") and resend it later.
Cryptographic Nonces: Every transaction incorporates a unique, single-use pseudorandom token string.
Monotonic Counters: Messages include sequentially increasing indexes, forcing the system to reject any duplicated or out-of-order data packets.

## Slide 13
NETWORK MICRO-SEGMENTATION
Containing Compromise
A compromised IoT node should not provide an attacker lateral access to critical corporate infrastructure layers.
Isolated Subnets: Field nodes must be kept on dedicated VLANs isolated from corporate workstations and sensitive asset databases.
Zero-Trust Architecture: Firewalls enforce strict access policies, restricting device traffic solely to authorized destination cloud endpoints and gateway servers.

## Slide 14
DEVICE ATTESTATION ARCHITECTURES
Remote Health Audits
Before a device is permitted to download configuration charts or fetch message blocks, its integrity must be verified remotely.
The Attestation Challenge: The cloud issues a random challenge payload token to the field node.
The Proof: The hardware sign module generates a cryptographic digest of the running memory map, proving the device is operating an unmodified, secure software stack.

## Slide 15
FIRMWARE VERIFICATION SCRIPT
Python validation logic

## Slide 16
SECURING THE SUPPLY CHAIN LIFECYCLE
Secure Factory Provisioning
Devices must be secured from the start, well before they are installed in a client environment.
Zero-Touch Staging: Unique cryptographic identities and mTLS device certificates must be injected into the silicon vault inside a trusted, secure manufacturing facility.
This prevents third-party contract manufacturers from copying the firmware image onto unauthorized clone hardware.

## Slide 17
TECHNICAL REVIEW QUESTIONS
How does a Hardware Root of Trust protect a remote device from runtime firmware modifications?
Explain why Mutual TLS (mTLS) is preferred over standard asymmetric encryption strategies in industrial IoT networks.
Describe the advantages of implementing a dual-partition memory layout for automated fallback during remote OTA updates.
Concept recap visual

## Slide 18
Defense in Depth for the Edge
Integrating secure hardware boundaries, strong cryptographic transport tunnels, and automated recovery loops builds resilient defenses against modern network threats.
QUESTIONS & DISCUSSION | END OF MASTERCLASS